## Slide 1: Memory Organization
Memory Hierarchy
  Memory hierarchy in a computer system :
    Main Memory : memory unit that communicates directly with the CPU (RAM)
    Auxiliary Memory : device that provide backup storage (Disk Drives)
    Cache Memory : special very-high-speed memory to increase the processing speed (Cache RAM)

## Slide 2: Memory Organization
  Multiprogramming
    enable the CPU to process a number of independent program concurrently
  Memory Management System :
    supervise the flow of information between auxiliary memory and main memory
Memory Hierarchy is to obtain the highest possible access speed while minimizing the total cost of the memory system
Register
Cache
Main Memory
Magnetic Disk
Magnetic Tape

## Slide 3: Random Access Memory (RAM)
  RAM Chips
  Static RAM
  Consists of Flip-flops to store binary information.
  Static RAM is easier to use and having short Read/Write cycles
  Used mostly in Cache memory.
  Dynamic RAM
  Stores binary information in the form of electric charge stored inside the capacitor.
  The capacitors are provided by MOS transistors.
  Refreshing circuit is required to refresh the memory.
  Dynamic RAM offers reduced power consumption and large storage capacity.
  It is used to construct main memory.
    Typical RAM chip :
      128 X 8 RAM : 27 = 128 (7 bit address lines)
    Typical ROM chip:
      512 X 8 ROM : 29 = 512 (9 bit address lines

## Slide 4: Static RAM Vs Dynamic RAM

## Slide 5: MAIN MEMORY
RAM and ROM Chips
Typical RAM chip
Typical ROM chip
Chip select 1
Chip select 2
Read
Write
7-bit address
CS1
CS2
RD
WR
AD 7
128 x 8
RAM
8-bit data bus
CS1 CS2 RD WR
0 0 x x
0 1 x x
1 0 0 0
1 0 0 1
1 0 1 x
1 1 x x
Memory function
Inhibit
Inhibit
Inhibit
Write
Read
Inhibit
State of data bus
High-impedence
High-impedence
High-impedence
Input data to RAM
Output data from RAM
High-impedence
Chip select 1
Chip select 2
9-bit address
CS1
CS2
AD 9
512 x 8
ROM
8-bit data bus
Main Memory

## Slide 6: MEMORY ADDRESS MAP
RAM 1
RAM 2
RAM 3
RAM 4
ROM
0000 - 007F
0080 - 00FF
0100 - 017F
0180 - 01FF
0200 - 03FF
Component
Hexadecimal
address
0 0 0 x x x x x x x
0 0 1 x x x x x x x
0 1 0 x x x x x x x
0 1 1 x x x x x x x
1 x x x x x x x x x
10 9 8 7 6 5 4 3 2 1
Address bus
Memory Connection to CPU
- RAM and ROM chips are connected to a CPU
through the data and address buses
- The low-order lines in the address bus select
the byte within the chips and other lines in the
address bus select a particular chip through
its chip select inputs
Address space assignment to each memory chip
Example: 512 bytes RAM and 512 bytes ROM
Main Memory

## Slide 7: CONNECTION OF MEMORY TO CPU
Main Memory
CS1
CS2
RD
WR
AD7
128 x 8
RAM 1
CS1
CS2
RD
WR
AD7
128 x 8
RAM 2
CS1
CS2
RD
WR
AD7
128 x 8
RAM 3
CS1
CS2
RD
WR
AD7
128 x 8
RAM 4
Decoder
3
2
1
0
WR
RD
9
8
7-1
10
16-11
Address bus
Data bus
CPU
CS1
CS2
512 x 8
ROM
AD9
1- 7
9
8
Data
Data
Data
Data
Data

## Slide 8: Numerical Problems
Q1. a) How many 128x8 RAM chips are needed to provide a memory capacity of 2048 bytes.
b) How any lines of the address bus must be used to access 2048 bytes of memory. How many of these lines will be common to all chips.
c) How many lines must be decoded for chip select? Specify the size of decoders.
Q2. Extend the memory system of Fig.1 to 4096 bytes of RAM and 4096 bytes of ROM. List the memory-address map and indicate what size decoders are needed.
Q3. A computer employs RAM chips of 256x8 and ROM chips of 1024x8. The computer system needs 2K bytes of RAM, 4K bytes of ROM, and four interface units each with four registers. A memory-mapped I/O configuration used. The two highest-order bits of the address bus are assigned 00 for RAM, 01 for ROM, and 10 for interface registers.
How many RAM and ROM chips are needed.
Draw a memory-address map for the system.
Give the address range in hexadecimal for RAM, ROM and interface.

## Slide 10: Cache Memory
12-5 Cache Memory
  Locality of Reference
    the references to memory tend to be confined within a few localized areas in memory
  Cache Memory : a fast small memory
    keeping the most frequently accessed instructions and data in the fast cache memory
  Hit Ratio
    the ratio of the number of hits divided by the total CPU references (hits + misses) to memory
      hit : the CPU finds the word in the cache
      miss : the word is not found in cache (CPU must read main memory)
  A computer with cache access time of 100ns, a main memory access time of 1000 ns, a hit ratio of 0.9 is having average access time of 200ns.

## Slide 11: Types of Mapping of Cache Memory
  Mapping
    The transformation of data from main memory to cache memory
      1) Associative mapping
      2) Direct mapping
      3) Set-associative mapping
  Associative Memory:
    main memory : 32 K x 12 bit word (15 bit address lines)
    cache memory : 512 x 12 bit word
      CPU sends a 15-bit address to cache
        Hit : CPU accepts the 12-bit data from cache
        Miss : CPU reads the data from main memory (then data is written to cache)

## Slide 12: Associative Memory

## Slide 13: Direct Mapping
  Direct mapping :
    n bit memory address
    Tag field (n - k) : Index field (k)
    2k words cache memory + 2n words main memory
        Tag = 6 bit (15 - 9), Index = 9 bit

## Slide 14: Direct Mapping
    Direct mapping cache with block size of 8 words :
      64 block x 8 word = 512 cache words size

## Slide 15: Set-Associative Mapping
  Set-associative mapping : (two-way)

## Slide 20: Questions
A two-way set associative cache memory uses blocks of four words. The cache can accommodate a total of 2048 words from main memory. The main memory size is 128Kx32. Formulate all pertinent information required to construct the cache memory. What is the size of cache memory.
A computer has a memory unit of 64Kx16 and a cache memory of 1K words. The cache uses direct mapping with a block size of four words. How many bits are there in the tag, index, block, and words fields of the address format. How many bits are there in each word of cache, and how are they divided into functions? Include a valid bit. How many blocks can the cache accommodate?
The access time of a cache memory is 100ns and that of main memory is 1000ns. It is estimated that 80 percent of the memory requests are for read and the remaining 20 percent for write. The hit ratio for read access only is 0.9. A write-through procedure is used. What is the average access time of the system considering only memory read cycles. What is the average access time of the system for both read and write requests. What is the hit ratio considering the write requests also.

## Slide 21: Answer

## Slide 22: Answer

## Slide 23
  Replacement Algorithm : cache miss or full
    1) LRU (Least Recently Used):
    2) Random Replacement:
    3) FIFO (First-In First-Out) :
  Writing to Cache :
      1) Write-through :
      2) Write-back :
  Cache Initialization
    Cache is initialized :
      1) When power is applied to the computer
      2) When main memory is loaded with a complete set of programs from auxiliary memory
      3) Cache is initialized by clearing all the valid bits to 0.
    Valid bit
      Indicate whether or not the word contains valid data

## Slide 24
VIRTUAL MEMORY
Give the programmer the illusion that the system has a very large memory,
even though the computer actually has a relatively small main memory
Address Space(Logical) and Memory Space(Physical)
Address Mapping
Memory Mapping Table for Virtual Address -> Physical Address
virtual address
(logical address)
physical address
address space
memory space
address generated by programs actual main memory address
Mapping
Virtual address
Virtual
address
register
Memory
mapping
table
Memory table
buffer register
Main memory
address
register
Main
memory
Main memory
buffer register
Physical
Address
Virtual Memory

## Slide 25: ADDRESS MAPPING
Organization of memory Mapping Table in a paged system
Address Space and Memory Space are each divided
into fixed size group of words called blocks or pages
1K words group
Page 0
Page 1
Page 2
Page 3
Page 4
Page 5
Page 6
Page 7
Block 3
Block 2
Block 1
Block 0
Address space
N = 8K = 213
Memory space
M = 4K = 212
0
000
1
001
1
010
0
011
0
100
1
101
1
110
0
111
1
Block 0
Block 1
Block 2
Block 3
MBR
0 1
0 1 0 1 0 1 0 0 1 1
1 0 1
0 1 0 1 0 1 0 0 1 1
Table
address
Presence
bit
Page no.
Offset
Virtual address
Main memory
address register
Memory page table
Main memory
11
00
01
10
01
Virtual Memory

## Slide 26: PAGE REPLACEMENT ALGORITHMS
FIFO
0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
7
0
1
0
0
7
1
2
0
1
2
3
1
2
3
0
4
3
0
4
2
0
4
2
3
0
2
3
0
1
3
0
1
2
7
1
2
7
0
2
7
0
1
Page frames
Reference string
FIFO algorithm selects the page that has been in memory the longest time
Optimal Replacement (OPT) - Lowest page fault rate of all algorithms
Replace that page which will not be used for the longest period of time
0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
7
0
1
0
0
7
1
2
0
1
2
0
3
2
4
3
2
0
3
2
0
1
7
0
1
Page frames
Reference string
Virtual Memory

## Slide 27: PAGE REPLACEMENT ALGORITHMS
- OPT is difficult to implement since it requires future knowledge
Replace that page which has not been
used for the longest period of time
LRU
0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
7
0
1
0
0
7
1
2
0
1
2
0
3
4
0
3
4
0
2
4
3
2
0
3
2
1
3
2
1
0
2
1
0
7
Page frames
Reference string
Virtual Memory

## Slide 28
A virtual memory system has an address space of 8K words, a memory space of 4K words and page & block sizes are of 1K words. The following page is referenced in memory: 4 2 0 1 2 6 1 4 0 1 0 2 3 5 7. Determine the four pages that are resident in main memory after each page reference change if page replacement algorithm is : FIFO, LRU, Optimal.
An address space is specified by 24 bits and the corresponding memory space by 16 bits. How many words are there in the address space. How many words are there in the memory space. If a page consists of 2K words, how many pages and blocks are there in the system?

## Slide 29: Secondary Storage

## Slide 30: Hard-disk Organization

## Slide 31: Magnetic Hard Disks

## Slide 32: Organization of Data on a Disk
Sector 0, track 0
Sector 3, track
n
Sector 0, track 1
Organization of one surface of a disk.
Access Time:
Seek time: Time required to move the R/W head to the proper track.
Rotational latency: Time required to move the starting position of sector under the read/write head.

## Slide 33: Optical Disks
Aluminum
Acrylic
Label
(a) Cross-section
Polycarbonate plastic
Source
Detector
Source
Detector
Source
Detector
No reflection
Reflection
Reflection
Pit
Land
0
0
0
1
0
0
0
0
1
0
0
0
1
0
0
1
0
0
1
0
(c) Stored binary pattern
Pit
Land
1
(b) Transition from pit to land

## Slide 34: Optical Disks
CD is 120 mm in diameter.
15 mm hole in the center.
Data stored on tracks that cover the area from 25 mm radius to 58 mm radius.
There are more than 15,000 tracks.
Spiral structured were unraveled will be more than 5 KM long !
Basic access speed is 1X, 75 sectors per second.
CD-RW:
Consists of alloy of silver, indium, antimony & tellurum.
When heated above 500c, it absorbs light.(Amorphous state)
When heated to 200c, it goes in crystalline state and allows light to pass through.

## Slide 35: Magnetic Tape Systems
Figure 5.33. Organization of data on magnetic tape.
File
File
mark
mark
File
7 or 9
gap
gap
File gap
Record
Record
Record
Record
bits
•
•
•
•
•
•
•
•

## Slide 36: Traditional Memory Architecture
Up to 2
k
addressable
MDR
MAR
Figure 5.1. Connection of the memory to the processor.
k
-bit
address bus
n
-bit
data bus
Control lines
( , MFC, etc.)
Processor
Memory
locations
Word length =
n
bits
W
R
/

## Slide 37: Internal Organization of Memory Chips
FF
Figure 5.2. Organization of bit cells in a memory chip.
circuit
Sense / Write
Address
decoder
FF
CS
cells
Memory
circuit
Sense / Write
Sense / Write
circuit
Data input
/output lines:
A
0
A
1
A
2
A
3
W
0
W
1
W
15
b
7
b
1
b
0
W
R
/
b
¢
7
b
¢
1
b
¢
0
b
7
b
1
b
0
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
16 words of 8 bits each: 16x8 memory org..
It has 16 external connections: addr. 4, data 8, control: 2, power/ground: 2

## Slide 38
A 2D Memory Chip
Figure 5.3. Organization of a 1K  1 memory chip.
CS
Sense
/
Write
circuitry
array
memory cell
address
5-bit row
input/output
Data
5-bit
decoder
address
5-bit column
address
10-bit
output multiplexer
32-to-1
input demultiplexer
32
32
X
W
R
/
W
0
W
1
W
31
and

## Slide 39: Some examples
For example:
4MB chip may have 512K X 8 organization, 19 address and 8 data lines.
Also 2^32 generates—4,294,967,296 values. Can address 4GB locations.

## Slide 40: Static RAM
The circuits are capable of retaining their state as long as power is applied.
Y
X
Word line
Bit lines
Figure 5.4. A static RAM cell.
b
T
2
T
1
b
¢

## Slide 41: Dynamic RAMs
Static RAMs are fast, but they cost more area and are more expensive.
Dynamic RAMs (DRAMs) are cheap and area efficient, but they can not retain their state indefinitely – need to be periodically refreshed.
Figure 5.6. A single-transistor dynamic memory cell
T
C
Word line
Bit line

## Slide 42: ROM Technology

## Slide 43: Read-Only-Memory (PROM)
Not connected to store a 1
Connected to store a 0
Figure 5.12. A ROM cell.
Word line
P
Bit line
T

## Slide 44: Read-Only-Memory
PROM: Programmable ROM
  Programmability is achieved by inserting a fuse at point P.
EPROM: Erasable, Programmable ROM
  Here, at point P special transistor is used which works as normal transistor or disabled transistor.
EEPROM: Electrically Erasable ROM.
  It can be programmed and erased electrically by applying appropriate voltages.

## Slide 45: Input-Output Organization
Peripheral Devices: Input & Output devices attached to computer are called Peripheral.
  Input Devices:
    Keyboard, Optical devices: Card reader, Bar code reader etc.
    Magnetic Input Devices: Magnetic stripe reader
    Screen Input Devices: Touch screen, Light pen etc.
  Output Devices:
    Keyboard, Optical devices: Card reader, Bar code reader etc.
    Peripherals that provide auxiliary storage are magnetic tape and magnetic disk.
    Input and output devices communicate alphanumeric information by using ASCII 7bit code.
    To use computer efficiently, large number of programs and data must be prepared in advance for execution with computer.
    Output Devices: CRT, Printer
    .

## Slide 46: Input-Output Interface
I/O interface provides a method for transferring information between internal storage and external I/O devices.
The purpose of interfacing are as follows:
  Peripherals are electromechanical & electromagnetic devices and are interacting with electronics devices(CPU).
  Data transfer rate of peripherals is usually slower than transfer rate of CPU.
  Data codes and formats in peripherals differ from word format in CPU
  Operating modes of peripherals are different from each other and each one must be controlled without disturbing other.
To resolve these differences, computer system includes Interface units between CPU and peripherals to supervise and synchronize all input and output transfers.

## Slide 47: Input-Output Interface
Each peripheral has its own controller that operates a particular electromechanical device.
To communicate with a particular device, the processor places a device address on the address lines.

## Slide 48: Input-Output Interface
When the interface detects it own address, it activates path between bus lines and the device.
At the time address is made available in address lines, the processor provides function code(I/O command) in the control lines.
Types of I/O command:
Control command: To activate and inform what to do.
Status command: To test various status conditions.
Data Output data: It causes the transfer of data from bus into one of its registers.
Data Input Command: Interface receives data from peripheral and places them on buffer register where it is put into data lines.

## Slide 49: I/O versus Memory Bus
In addition to communicating to I/O, processor must also communicate with memory unit.
There are three ways that computer buses can be used to communicate with memory and I/O:
  Use two separate buses, one for memory and one for I/O. (IOP)
  Use one common bus for both memory and I/O but have separate control lines for each. (Isolated I/O)
  Use one common bus for memory and I/O with common control lines. (Memory Mapped I/O)

## Slide 50: Isolated I/O
The distinction between memory and I/O transfer is made through separate read and control lines.
I/O read and I/O write are enabled during I/O transfer and Memory read/write are enabled during memory transfer.
In the isolated I/O configuration, CPU have distinct input and output instructions where each of it will be associated with address of the interface register.
When the CPU fetches and decodes the I/O instruction, it places the address associated with the instruction on the common address lines and enables I/O read or I/O write control line.
When the CPU fetches and decodes the Memory instruction, it places the address associated with the instruction on the common address lines and enables Memory read or Memory write control line.
The isolated I/O method isolates memory and I/O addresses.

## Slide 51: Memory Mapped I/O
Here the same address space is used for both memory and I/O. The computer treats interface register as a part of memory system.
The assigned address cannot be used for storing memory words, which reduces memory address range available.
In a memory-mapped I/O organization, there are no specific, input or output instruction.
CPU manipulate I/O data residing in interface registers with the same instruction used to manipulate memory words.
Load and store instruction used for reading/writing from memory and can be use for input or output data from I/O instruction.
With memory-mapped I/O all instructions that refer to memory are also available for I/O.

## Slide 52: Memory Mapped I/O

## Slide 53: Modes of Transfer
Data transfer between the CPU and the I/O devices may be handled in variety of modes. Some modes use the CPU as an intermediate path and others transfer the data directly to and from the memory unit.
Data transfer to and from peripherals may be handled in three ways:
  Programmed I/O
  Interrupt-initiated I/O
  Direct Memory Access (DMA)

## Slide 54: Programmed I/O
Programmed I/O operations are the result of I/O instructions. Each data item transfer is initiate by an instruction in the program.
Usually the transfer is to and from a CPU register and peripheral. Other instructions are needed to transfer data between memory and CPU.
Once a data transfer is initiated, the CPU is required to monitor the interface to see when a transfer can again be made.

## Slide 55: Programmed I/O

## Slide 56: Interrupt Initiated I/O
In the programmed I/O CPU stays in program loop until the I/O indicates that it is ready for data transfer.
This is time consuming process since it makes CPU busy needlessly.
This can be avoided by using an interrupt facility.
When the interface determines that device is ready for data transfer, it generates an interrupt request.
Upon detecting external interrupt signal, the CPU momentarily stops the task it is processing.
It then branches to fulfill the I/O request and return to the original task.
Based on the concept of Priority Interrupt.

## Slide 57: Direct Memory Access (DMA)
The transfer of data between a fast storage device such as magnetic disk and memory often limited to the speed of CPU.
Removing the CPU and letting the peripheral device manage the memory bus directly improve speed of transfer.
Such transfer technique is called Direct Memory Access (DMA).
A DMA controller takes over the buses to manage the transfer directly between I/O device and memory.
During DMA transfer, the CPU is idle and has no control over memory buses.
By using Bus Request(BR) and Bus Grant(BG) the buses are released to DMA controller.

## Slide 58: DMA
Data transfer ways:
  Burst Transfer: Here number of words are transferred in a block. Example: Magnetic disk.
  Cycle stealing: Allows the DMA controller to transfer one data word at a time after it must return the control of buses to CPU.

## Slide 59: DMA Controller

## Slide 60: Initialization of DMA
The CPU initializes the DMA by sending the following information through the data bus.
  The starting address of the memory block where data are available(for read) or where data are to be stored(for write).
  The word count, which is the number of words in the memory block.
  Control to specify the mode of transfer such as read or write.
  A control to start the DMA transfer.

## Slide 61: DMA Transfer in a computer system

## Slide 62: Input-Output Transfer (IOP)

## Slide 63: Input-Output Transfer (IOP)
An IOP takes care of input and output tasks.
IOP is similar to CPU except IOP can fetch and execute an I/O instruction.
CPU is usually assigned task of initiating the I/O program and thus IOP.
The CPU is assigned the task of initiating all operations, but I/O instructions are executed in IOP.
When an I/O operation is required, the CPU informs the IOP where to find the I/O program and then leaves the transfer details to the IOP.
CPU instructions also test I/O status conditions needed for making decisions on various I/O activities.
IOP is also responsible of taking care of data synchronization, formats etc between CPU and I/O devices.
In most computers CPU is master and IOP is slave.
The IOP typically asks for CPU attention by means of Interrupt.

## Slide 64: Bus Arbitration
The device that is allowed to initiate data transfers on the bus at any given time is called Bus master.
Bus arbitration is the process by which the next device becomes Bus master and will do the data transfer.
Two approaches: Centralized Arbitration and Distributed Arbitration.
        Centralized Arbitration

## Slide 65: Types of Interrupt
Major types of Interrupt are:
  External Interrupt: It comes from I/O devices, from timing device, or from any other external source. Example that cause
  Internal Interrupt: It includes register overflow, invalid operation code, stack overflow etc.
  Software Interrupt or Hardware Interrupt: External and Internal interrupts are initiated from signals that occur in the hardware of the CPU. A software interrupt is initiated by executing an instruction.
  Priority Interrupt: In case several sources will request service simultaneously, in this case system must decide which device to service first. For ex: Polling, Daisy Chain.

## Slide 66: Buses
Data Bus: Bi-directional and transfers data.
Address Bus: Uni-directional and sends the address.
Control Bus: R/W, BR,BG etc.
Bus Structure: Single bus

## Slide 67: Buses
Bus Structure: Multi bus

## Slide 68: Synchronous or Asynchronous Data Transfer
Internal operations in a digital system are synchronized by means of clock pulses supplied by common pulse generator.
If the registers in the interface share a common clock with the CPU registers, the transfer is synchronous.
Asynchronous data transfer requires that control signals be transmitted between communicating units to indicate the time at which data is being transmitted.
Asynchronous data transfer can be accomplished by Strobe & Handshaking.

## Slide 69: Strobe Control
Strobe control:
  It employs single control line.
  It can be activated either by source or destination unit.

## Slide 70: Handshaking